TERM OF REFERENCE OF THE PUBLIC CALL FOR PURCHASE OF NATURAL GAS

- OBJECT OF THE CALL FOR PROPOSALS

Companhia de Gás do Ceará – CEGÁS, the exclusive concessionaire of local piped gas services in the State of Ceará, announces that it intends to acquire NATURAL GAS, independent of its origin (onshore, offshore and Liquefied Natural Gas (LNG), etc.), according to supply requirements and the conditions set out in this Term, through a CALL FOR PROPOSALS from BIDDING COMPANIES.

This CALL FOR PROPOSALS is being coordinated by the LOCAL PIPED GAS DISTRIBUTION COMPANIES of the following states:

  - Alagoas - Gás de Alagoas S.A. - Algás

  - Bahia - Companhia de Gás da Bahia – Bahiagás

  - Ceará - Companhia de Gás do Ceará – Cegás

  - Paraíba - Companhia Paraibana de Gás – Pbgás

  - Pernambuco - Companhia Pernambucana de Gás – Copergás

  - Rio Grande do Norte - Companhia Potiguar de Gás – Potigás

  - Sergipe - Sergipe Gás S.A. – Sergas

- TERMINOLOGY

For a better understanding, the terms in capital letters, whether in the singular or plural, will be defined as follows:

LOCAL PIPED GAS DISTRIBUTION COMPANY or LDC: means the Companhia de Gás do Ceará – CEGÁS, the company holding the public concession for local piped gas services in Ceará, in compliance with Section 2 of article 25 of the Federal Constitution.

REFERENCE CONDITIONS – means the temperature of 20ºC (twenty degrees Celsius), absolute pressure of 101.325 Pa (one hundred and one thousand, three hundred and twenty-five Pascal) and superior calorific power (SCP), on a dry basis for gas equal to 9,400 kcal/m³ (nine thousand, four hundred kilocalories per cubic metre).

BIDDING COMPANY – Company interested in taking part in the Call for Proposals process to supply NATURAL GAS to the LDC, as per the conditions established in the Public Notice and this Term of Reference.

REMOVAL GUARANTEE – Volume of GAS, in the REFERENCE

CONDITIONS, which the LDC undertakes to remove on a daily, weekly, monthly or annual basis, as expressly established in a contract.

GAS OR NATURAL GAS – means the mixture of hydrocarbons essentially made up of methane, other hydrocarbons and non-combustible gases, which is extracted from natural reservoirs and remains in a gaseous state in normal atmospheric conditions.

LIQUEFIED NATURAL GAS OR LNG: NATURAL GAS submitted to a liquefaction process for storage and transportation, which can be regasified at its units;

FIRM-BASIS OR FB CONTRACT TYPE: Type of contract with a greater GUARANTEE OF CONTRACTED GAS REMOVAL, in order to meet the basis of GAS demand in the LDC market.

SEASONAL OR SZ CONTRACT TYPE: Type of contract with a lower REMOVAL GUARANTEE than a FB contract, in order to meet the cyclical variations in GAS demand in the LDC market.

AVAILABILITY OR DS CONTRACT TYPE: Type of contract with a lower REMOVAL GUARANTEE than a SZ contract, in order to meet intermittent GAS demands in the LDC market (e.g. demand for GAS for thermal plant orders).

CUSTOMIZED OR CT CONTRACT TYPE: Type of contract, which is not applicable to the other types, with the conditions freely negotiated by the parties.

POINT OF DELIVERY OR CUSTODY TRANSFER STATION – comprises the

installations required for the availability of GAS by the bidding company to the LDC, in the REFERENCE CONDITIONS, where there is a GAS custody transfer.

RECEIVING POINT – Point on Brazilian territory in which the GAS in the Bidding Company’s possession will be transferred to the custody of the Carrier, so that it begins its transportation to the POINT OF DELIVERY.

CONTRACT LOT – A set of contract conditions defined in the Call for Proposals public notice for which interested Bidding Companies can present Gas Supply Contract proposals, represented by the codes AA CC DDDD A-E/FF, where:

AA corresponds to the abbreviation for the LDC’s State;

CC corresponds to the Contract Type (FB, SZ, DS or CT);

DDDD corresponds to the daily quantity of GAS in the REFERENCE CONDITIONS to be contracted, given in thousand m³/day;

A-E corresponds to the number of years preceding the start of the planned supply from the date of the Call for Proposals (e.g.: one year in advance: A-1);

FF corresponds to the number of years of the Contract period.

- POINT OF DELIVERY OR CUSTODY TRANSFER STATION

The DELIVERY POINTS located in Ceará are described in Table 1:

Table1 – List of the Points of Delivery in Ceará

| Point of Delivery Code | Name | Municipality | Observations |
| --- | --- | --- | --- |
| 1 | PE-Aquiraz | Aquiraz | Metropolitan Region of Fortaleza |
| 2 | PE-Fortaleza | Maracanaú | Metropolitan Region of Fortaleza |
| 3 | PE-Pacajus | Pacajus | Metropolitan Region of Fortaleza |
| 4 | PE-Pecém | São Gonçalo do Amarante | Metropolitan Region of Fortaleza |
| 5 | PE-Caucaia | Caucaia | Metropolitan Region of Fortaleza |
| 6 | PE-Aracati | Aracati | - |

For a NATURAL GAS BIDDING COMPANY via LNG, the LNG terminals in operation on the date scheduled to supply GAS from the LDC CONTRACT LOTS can be considered the POINT OF DELIVERY. The  LDC, together with the BIDDING COMPANY, will perform a technical and economic viability study for this supply.

The BIDDING COMPANY may suggest an alternative POINT OF DELIVERY to those mentioned above, with the LDC being responsible, together with the BIDDING COMPANY for performing a technical and economic viability study.

It is highlighted that, having observed the conditions established in the Concession Contract, the LDC may make an investment in order to receive the natural GAS closer to the production area or regasification unit, where distribution network infrastructure may not currently exist.

The LDC will define the connection regulations with the distribution network in a specific document and/or a Purchase and Sale Agreement.

- CONTRACT LOTS

For this Call for Proposals, the LDC will receive offers to contract the supply of GAS In contract type(s) and other conditions defined in the following CONTRACT LOT(S):

| LOTE 01: CE FB 0600 A-2/5 |
| --- |
| Estado | Modalidade | Volume de Suprimento | Início do fornecimento | Prazo de contratação |
| CE | Firme Base | 600.000 m³/dia | 01/01/2020 | 5 anos |
| Obs.: |

The LDC will send Information on the CONTRACT LOTS by POINT OF DELIVERY following receipt of the BIDDING COMPANY’S DECLARATION OF INTEREST AND CONFIDENTIALITY.

If the BIDDING COMPANY is interested in presenting one or more proposals with conditions different to those established in the above-mentioned CONTRACT LOTS, it can do this freely, with the LDC being responsible for analyzing its interest in the proposal.

- QUALITY OF THE GAS SUPPLIED

The natural GAS must meet the needs of the quality requirements established in the National Agency of Petroleum, Natural Gas and Biofuels (ANP) Resolution Nº 16/2008 or its replacement.

The BIDDING COMPANY should present the NATURAL GAS quality analyses through a laboratory with valid National Institute of Metrology, Quality and Technology (INMETRO) accreditation, according to the requirements established in the Brazilian Association of Technical Standards (ABNT) Standard ISO/IEC 17025:2005.

- RELIABILITY OF THE NATURAL GAS PROVISION

The BIDDING COMPANY should present a Certification of Proven NATURAL GAS Reserves Report produced by an independent consultancy firm and an Annual Reserve Bulletin registered at the ANP.

For cases of sales through LNG, proof of the availability of GAS abroad and of its capacity to deliver LNG in Brazil must be presented.

- PRICES AND COMMERCIAL CONDITIONS

The BIDDING COMPANY should present an initial proposal for the price  of GAS in its REFERENCE CONDITION (excluding taxes), delivered to one of the POINTS OF DELIVERY listed in item 3 or at a CUSTODY REFERENCE STATION to be constructed by the LDC, if this is the case.

The price of the GAS should be expressed in Reais per cubic metre (R$/m³) or Dollar per million British Thermal Units (BTU - US$/MMBTU) for each CONTRACT LOT.

The cost of transporting GAS in the REFERENCE CONDITION in R$/m³, which corresponds to all the costs incurred by the BIDDING COMPANY to move the GAS on Brazilian territory between the POINT OF RECEIPT and POINT OF DELIVERY should be detailed in the proposal.

The definitive questions involving the price of natural GAS and the commercial conditions for the GAS will be specified in the draft Purchase and Sale Agreement in due course.

- OTHER CONDITIONS

The BIDDING COMPANY will not have any right to reimbursement for any costs related to taking part in this Call for Proposals.

Participation in the Call for Proposals does not bind any of the parties, nor does it generate any commitment for the LDC to acquire GAS.

If delivery of the NATURAL GAS is by road, this should be performed through a station owned by the BIDDING COMPANY and connected to the LDC network.

If the offer is through LNG, the BIDDING COMPANY should be responsible for contracting all the stages until delivery of the fuel to the LDC, and the price offered should take into account all the costs to the POINT OF DELIVERY.

The LDC reserves the right to modify the conditions of the Call for Proposals or cancel it at any time, advising the bidders of these facts.

In the case of a judicial decision or by another competent public authority stipulating demonstration of the proposal presented, the LDC will request that the respective proceedings are in camera legal proceedings, in order to guarantee the confidentiality of the proposals.

The proposals, which the LDC considers of interest, may lead to the signature of a Letter of Intent or Memorandum of Understanding (MOU), which will detail the commercial and technical conditions; once this stage is completed, a GAS Purchase and Sale Agreement may be signed between the parties, under the terms of current legislation.

- INSTRUCTIONS TO TAKE PART IN THE CALL FOR PROPOSALS

The BIDDING COMPANY should send its COMMERCIAL PROPOSAL FOR THE SALE OF NATURAL GAS to the following email suprimentogn@cegas.com.br, until 5:00 pm on 08/11/2018, as per the conditions established in this Call for Proposals signed by its legal representatives and forwarded to the LDC CEO.

- CONTACT

Any communication and requests for additional information can be made through the following email address: suprimentogn@cegas.com.br.

HUGO SANTANA DE FIGUEIRÊDO JUNIOR

CEO of CEGÁS